## Slide 1: Bootrom (Public/Secure) Boot sequence from power-on to Linux

## Slide 2: Scope
Startup of system domain.
HW & SW design – boot related functions.

## Slide 3: Boot Modes
USB Boot.
eMMC Boot.
Selected by an external pin setting.

## Slide 4: Stages
1st Stage: Boot ROM code and Loader Execution.
  Starts execution from Mask Secure ROM.
  Select bootable interface(USB / eMMC) and initialize it.
  Do security checks of the images downloaded.
  Flash SW image into eMMC (only for USB mode).
2nd Stage: Domain Setup.
  Each domain(System, RT and Modem) starts running from external SDRAM.

## Slide 5: Memory Used at Boot Time
Mode | Memory Type | Size in (Kbytes)
Non Secure | Public ROM | 64
Secure | Secure ROM | 96
 | Secure RAM | 256
Non Secure - Secure | Inter connect RAM | 72
Common | L1 I-Cache | 32
 | L1 D-Cache | 32
 | L2 Cache | 256
 | S3Cache (MERAM) | 2048

## Slide 6: HW Architecture Outline

## Slide 7: SW Architecture Outline
Public ROM Service
Secure Side
Public Side
Secure ROM Service
S3Cache (MERAM)
RAMSET
R-loader (eMMC)
FW Uploader
SA
ISSW
Test Certificate
Secure RAM
Renasas Library
Crypto Lib
Device Driver
Secure ROM
Libraries
Other HW
Crypto HW
Security
Library API
ISSW API
ROM
Loader
[ NOTE ]
- For public ROM internal use
- Provides access for Secure mode, and called only by Public ROM for security reasons.
- Communication btw S & NS mode uses shared memory called Inter connect RAM
- Load verify and execute ISSW.
- Also initialize secure resources.
- Handles entry/exit from/to S/NS modes
To access HW resources(crypto engines) from Secure ROM service
- Used in both boot cases.
- Patch code for Public ROM
- OEMs also use RAMSET in order to some early changes in clk config for example.
- Initial Security Software
- 1st external SW executed in secure mode.
- Initialization of secure peripherals
- Loading/authenticating of 2nd image.
- SA(Secure Application) – loaded by ISSW
- Application SW that is executed in secure mode.
- TC (Testing Certificate)
- Includes bit pattern for enable/disable debug interfaces such as JTAG, STM
- According to this parameter ISSW enables/disables the debug functionality.
- eMMC boot only
- Perform SBSC settings.
- Download OS image to SDRAM.
- USB boot only
- Donwload SW via USB interface and program into eMMC device.

## Slide 8: High Level Boot Sequence
Public Mode
Secure Mode
Cpu initialization
Secure peripheral init
Cpu initialization
Boot interface selection
eMMC initalization
Load 1st Image
SSA_ISSW_IMPORT
Authenticate ISSW
Import to secure RAM
ISSW_init
As per TC enable debug
Authenticate Ramset
Execute R-loader
Initialize DDR
Return response
Authenticate 2nd image
Import SA to secure RAM
Execute Ramset
Load 2nd image

## Slide 10: eMMC Partition Structure

## Slide 11: Low Battery
Taken care by R-loader
Check current voltage, if enough perform normal boot.
If voltage not enough, but VBUS is not detected, perform poweroff.
If voltage not enough, VBUS detected, load off_charging module.